## Slide 1
16-bit vs 32-bit MIPS Processor
Algorithmic Complexity vs Data Width
Ricardo Herrera-Pineda, Sean Wygant,
Daniel Mondragon, Heba Hafez
CPP Computer Engineering

## Slide 2
Project Overview
What We Built
Two complete MIPS processors on FPGA:
• 16-bit single-cycle MIPS
• 32-bit single-cycle MIPS
Goal: Compare resource utilization and performance
to understand the trade-offs between data width
and algorithmic complexity

## Slide 3
Research Questions
RQ1: Does data path width directly correlate with hardware resource utilization?
RQ2: How do algorithmic design choices impact resource consumption independent of data width?
RQ3: What are the performance implications of different branch calculation strategies?
RQ4: Can these findings inform future educational processor implementations?

## Slide 4
Our Approach: Implementation
Step 1: Design & Build
16-Bit MIPS
• 8 registers
• 16-bit data path
• 13 instructions
• Complex branch logic
(6 operations)
32-Bit MIPS
• 32 registers
• 32-bit data path
• 13 instructions
• Simple branch logic
(2 operations)

## Slide 5
Our Approach: Testing & Measurement
Step 2: Measure Everything
• Hardware Resources:
LUTs, Flip-Flops, I/O
• Power Consumption:
Dynamic, Static, Total
• Timing Analysis:
Endpoints, Critical Paths
• Performance:
Instruction Count, Execution Time

## Slide 6
Key Finding: The Paradox
16-bit uses MORE resources than 32-bit!
414 LUTs vs 376 LUTs (+10%)
Expected: Narrower = Fewer resources ✗
Reality: Complex algorithm = More resources ✓

## Slide 7
Results: Resource Utilization
Metric
16-Bit
32-Bit
Winner
LUTs
414
376
32-bit ✓
Flip-Flops
116
196
16-bit ✓
Logic Power
0.126 W
0.120 W
32-bit ✓
Endpoints
887
551
32-bit ✓
Pattern: 32-bit wins on logic efficiency (LUTs, power, endpoints)

## Slide 8
Results: Performance
Instructions Executed
16-bit: 20,354
32-bit: 16,836
→ 21% fewer (32-bit)
Execution Time
16-bit: 8.07 s
32-bit: 6.70 s
→ 21% faster (32-bit)
Energy Consumed
16-bit: 6.72 J
32-bit: 5.78 J
→ 14% less (32-bit)

## Slide 9
Root Cause: Branch Calculation
Why does 16-bit use MORE LUTs?
16-Bit Branch Logic
1. Shift immediate
2. Check if negative
3. Negate (NOT + 1)
4. Subtract OR Add
5. Multiplex result
Total: 6 operations
~90 LUTs needed
32-Bit Branch Logic
1. Shift immediate
2. Add to PC
Total: 2 operations
~40 LUTs needed

## Slide 10
Key Insights
Algorithmic Efficiency > Data Width
Smart algorithms beat brute-force narrowing
Trust Hardware Features
Using signed arithmetic is more efficient than manual implementation
Consistency Across Metrics
LUTs, power, timing, and performance all confirm the same pattern
Educational Value
Demonstrates that design choices matter more than architectural width

## Slide 11
Answering Our Research Questions
RQ1: Data width vs resources?
→ NO - 16-bit uses MORE despite being narrower
RQ2: Algorithmic choices?
→ YES - Algorithm dominates (6 ops vs 2 ops)
RQ3: Performance implications?
→ SIGNIFICANT - 21% faster, 14% less energy
RQ4: Educational insights?
→ YES - Teaches optimization principles

## Slide 12
Conclusion
Smart Design Beats Brute-Force Narrowing
✓ 32-bit processor is more efficient overall
✓ Algorithmic complexity matters more than data width
✓ Trust hardware features (signed arithmetic)
✓ Practical lesson for future processor designs

## Slide 13
Thank You!
Questions?
Ricardo Herrera-Pineda, Sean Wygant,
Daniel Mondragon, Heba Hafez